## Slide 1
Fuels and uses

## Slide 2
Outline
Fuels efficiency
Fuels for electricity
Fuels for transport

## Slide 3
Choosing a fuel
Fuel needs to be fit for purpose
Factors to consider:
    Energy released per unit mass or volume and emissions
    Availability and cost of fuel
    Ease of transport
    Hazards to people and the environment associated with its use and its waste products
    Social, economic, cultural and political values that can affect the choice of the fuel

## Slide 4
Intended use and fuel choices
NASA used liquid hydrogen to fuel the Saturn rockets
It produces a large quantity of energy per gram

## Slide 5
Fuel efficiency
Percentage of the energy converted to useful energy
E.g if a roof top solar panels have an efficiency of 17 %, so 17 % of the energy of the sun is converted into electrical energy and 83 % is mostly converted to heat energy (simply increasing the temperature of the cell)

## Slide 6
Electricity production
From coal
  Three quarters of Australian electricity is from coal
  The equation for the combustion of coal is:
  C(s) + O2(g)  CO2(g)
  Energy released: ~ 32 kJ g-1
  Overall efficiency is 30 -40 % (remainder is lost as heat)

## Slide 7
Electricity production
From natural gas
  Used in WA, burn methane and other small alkanes
  Composition varies but is mostly methane:
  CH4(g) + 2O2(g)  CO2(g) + 2H2O(g)
  Energy released: ~ 55.6 kJ g-1
  Overall efficiency just over 40 %, and releases less emission

## Slide 8
Electricity production
From biogas
  New renewable source of methane
  Composition of methane:
  CH4(g) + 2O2(g)  CO2(g) + 2H2O(g)
  Small scale operations typically located at the site the gas is produced (e.g. sewage plants, large animal farms)

## Slide 9
Fuel for transport
From petrol
  Mixture of hydrocarbons including octane
  Composition varies but combustion of octane is:
  2C8H18(g) + 25O2(g)  16CO2(g) + 18H2O(g)
  Energy released: ~ 47.8 kJ g-1
  Overall efficiency can be as high as 25 %

## Slide 10
Fuel for transport
From liquid petroleum gas (LPG)
  Mixture of hydrocarbons mostly propane
  Composition varies but combustion of propane is:
  C3H8(g) + 5O2(g)  3CO2(g) + 4H2O(g)
  Energy released: ~ 50.5 kJ g-1
  Use a standard petrol engine fitted with gas tank and a modified fuel injection system
  LPG is cheaper then petrol but the modifications are expensive and the tank takes up a lot of space

## Slide 11
Fuel for transport
From bioethanol
  Australia is reliant on fuel imports, bioethanol production could see more production here
  Composition varies but combustion of ethanol is:
  C2H5OH(l) + 3O2(g)  2CO2(g) + 3H2O(g)
  Energy released: ~ 29.7 kJ g-1
  Energy content of ethanol is about 62 % that of petrol, so need much greater of volume of ethanol
  Ethanol is already partly oxidised

## Slide 12
Fuel efficiency

## Slide 13
On going work
Pearson 11.3 review and the chapter 11 review
STAWA sets 29